Model Independent Analysis:
van Holde – Weischet Analysis
[Speaker Notes: Diffusion can obscure the presence of solute heterogeneity, and needs to be separated from sedimentation effects through analysis. Multiple scans are required for this analysis.]

---
What about Diffusion and Heterogeneity?
[Speaker Notes: Diffusion can obscure the presence of solute heterogeneity, and needs to be separated from sedimentation effects through analysis. Multiple scans are required for this analysis.]

---
Enhanced van Holde – Weischet Method:
Description of the Problem:
How do we distinguish between transport due to diffusion and transport due to sedimentation?
How do we distinguish boundary spreading due to heterogeneity from boundary spreading due to diffusion?
For unknown samples, can we analyze the sample in a model-independent way?

---
Enhanced van Holde – Weischet Method:
...is a graphical transformation of the velocity data:
transport due to Diffusion ~
transport due to sedimentation ~
At infinity transport due to diffusion will be negligible compared to transport due to sedimentation - i.e., all components will separate out if the rotorspeed is fast enough.
...yields diffusion corrected sedimentation coefficient distributions
van Holde, K. E. and W. O. Weischet. (1978). Boundary Analysis of Sedimentation Velocity Experiments with Monodisperse and Paucidisperse Solutes. Biopolymers, 17:1387-1403
Demeler, B. and K. E. van Holde. Sedimentation velocity analysis of highly heterogeneous systems. (2004). Anal. Biochem. Vol 335(2):279-288
sqrt t
t

---
Calculation of apparent Sedimentation Coefficients:
hat s `_b ~=~ ln {( {r_b`(t)} over {r_a ` (t_0)})} ~ [%omega^2`(t`-t_0)]^{`-1}
v over {%omega^2 r} ~= ~ s
dr over r ~= %omega^2 ` s ` dt
[Speaker Notes: An apparent sedimentation coefficient for each radial point in the scan boundary can be determined from the position, time and rotor speed. Equally spaced divisions are made between the baseline and the plateau of the scan, and radial positions of their intercepts with the boundary are used together with the corrected time of the scan to calculate an apparent sedimentation coefficient for each point in the boundary.]

---
[Speaker Notes: An apparent sedimentation coefficient for each radial point in the scan boundary can be determined from the position, time and rotor speed. Equally spaced divisions are made between the baseline and the plateau of the scan, and radial positions of their intercepts with the boundary are used together with the corrected time of the scan to calculate an apparent sedimentation coefficient for each point in the boundary.]

---
van Holde – Weischet Extrapolation Plot:

---
van Holde – Weischet Extrapolation Plot:
Scan 1 – start
of Experiment
[Speaker Notes: van Holde – Weischet extrapolation plot of a two-component system (lysozyme and a 208 bp DNA fragment). Apparent sedimentation coefficients from corresponding divisions are extrapolated to infinite time (zero on a timescale of 1/squareroot of time). Intercepts on this graph are the diffusion-corrected sedimentation coefficients of all components in the system. Extrapolations from different parts in the boundary pointing to the same intercept correspond to the same component. Different intercepts correspond to heterogeneity. Note the spread of the “fan plot” is different for the two components. The lower (1.8 s) component has a much broader fan plot than the upper fan plot (5.1 s). This is due to the difference in diffusion coefficients in the two components. A broader “fan” indicates a larger diffusion coefficient.]

---
van Holde – Weischet Extrapolation Plot:
Scan 10 – middle
of Experiment

---
van Holde – Weischet Extrapolation Plot:
Scan 20 – end
of Experiment

---
van Holde – Weischet Extrapolation Plot:
Division 1
(Baseline)
Boundary
Fraction = 5%

---
van Holde – Weischet Extrapolation Plot:
Boundary
Fraction = 50%
Division 10
(Midpoint)

---
van Holde – Weischet Extrapolation Plot:
Boundary
Fraction = 95%
Division 20
(Plateau)

---
van Holde – Weischet Integral Distribution Plot (G(s)):
[Speaker Notes: When plotting the intercepts against the boundary divisions, a quantitative measure of the partial concentrations is obtained that can be directly read off of the Y-axis]

---
Enhanced van Holde – Weischet Method:
van Holde – Weischet method:
s1:	5.35 x 10-13 (52 %)
s2:	1.87 x 10-13 (39 %)
[Speaker Notes: The van Holde – Weischet method provides a model-independent graphical transformation of the experimental data. The analysis results in an integral sedimentation coefficient distribution that can be used to read off distribution data in either a chromatogram-like profile (blue) or an integral distribution plot, which provides directly the relative concentration of each species (red).]

---
Enhanced van Holde – Weischet Method:
Green: Back diffusion distorts boundary – data points are excluded
Cyan: boundary has not cleared meniscus – data points are excluded
[Speaker Notes: Back-diffusion from the bottom of the cell causes distortions in the plateau region near the bottom of the cell. It is therefore important to exclude the data which may be affected by back-diffusion of the concentration gradient building up at the bottom of the cell. The green circle highlights the region that need to be investigated. The program will find out how far the smallest s-value species will diffuse back into the cell, assuming it is spherical. The red line indicates the separation between the distance the smallest species could have diffused back into the cell and the region that is not affected (based on a user selected tolerance value). Boundary segments between the bottom of the cell and the red line are ignored by the program and corresponding boundary divisions are not calculated. Slow sedimentation prevents some of the boundary to clear the meniscus and hence no boundary exists to calculate apparent sedimentation coefficients in that boundary fraction. The region highlighted in cyan shows where corresponding values are omitted and hence are missing in the plot.]

---
Application Examples:
van Holde – Weischet Analysis Application Examples:
Concentration dependent nonideality of s.
Aggregation and irreversible self-association
Composition Analysis
Reversibly Self-Associating Systems vs. non-interacting systems
Stoichiometry of Association
Relative quantification of individual components
Conformational information

---
Concentration Dependency of the Sedimentation Coefficient
[Speaker Notes: Concentration dependency of s causes higher concentrated sample to sediment slower than lower concentrated sample. As a result, material sedimenting in the upper boundary portion sediments slower than material sedimenting near the baseline. The blue line shows a sample without concentration dependency, the red line shows a sample with concentration dependency.]

---
Concentration Dependency of the Sedimentation Coefficient
[Speaker Notes: Because a concentration dependent sample sediments slower at higher concentration, extrapolation of points in the upper boundary portion point to lower S-values than extrapolations of points in the lower concentration portion of the boundary. This gives rise to a “crossover” point, indicated by the “*”.]

---
Concentration Dependency of the Sedimentation Coefficient
[Speaker Notes: Integral distribution plots of concentration dependent samples have a negative slope. Please not that extrapolation of each line to zero concentration does not reproduce a true s0 value. Please note that the negative slope of the integral distribution plot of a concentration dependent sample can be obscured or compensated by heterogeneity, giving rise to vertical or positive slopes in the integral distribution plots. To exclude this possibility, always run multiple concentrations. In a non-interacting system, multiple concentrations will produce identical distributions in each case. A heterogeneous system of concentration dependent samples will have a higher weight average sedimentation coefficient at lower concentration than at high concentration, and a reversibly self-associating system will show higher weight average sedimentation coefficients for higher concentrations.]

---
Concentration Dependency of the Sedimentation Coefficient
[Speaker Notes: A true s0 value can be obtained by measuring multiple concentrations of the same sample and extrapolation corresponding concentrations from the integral distribution plot to zero concentration.]

---
van Holde – Weischet Analysis: Limitations
The van Holde – Weischet method cannot be used for fitting diffusion coefficients, molecular weights, association constants or frictional coefficients, only sedimentation coefficients and partial concentrations are reported.

---
van Holde – Weischet Applications: Summary
  Model independent analysis
  Initial characterization of an unknown sample
  Composition analysis:
Homogeneous or heterogeneous?
Aggregation?
Binding Stoichiometry
Molecular weight distribution transformations
Relative quantification of individual components
  Conformational analysis
  Qualitative information about diffusion
  Identify concentration dependency:
Self-association or non-interacting?
Reversible or irreversible?
Concentration dependent solution nonideality?